## Slide 1
Interview Study Guide: Encryption and Advanced Technologies

## Slide 2
Q&A
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 3
Q
A
Q: What are BGP and OSPF used for?
A:
BGP (Border Gateway Protocol): Exterior routing protocol, controls how packets are routed across the internet between autonomous systems. Path-vector, scalable, policy-based.
OSPF (Open Shortest Path First): Interior routing protocol for enterprises. Link-state, uses cost as metric, converges quickly.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 4
Q
A
Q: If a customer wants to connect multiple branches securely over SD-WAN with dynamic routing, would you use OSPF or BGP, and why?
A:
It depends on scale and design.
OSPF → Best for smaller deployments inside the enterprise.
Link-state protocol calculates paths by cost and converges quickly.
Efficient for LAN/WAN routing.
BGP → Best for larger multi-branch or multi-ISP environments.
Policy-based, scalable, redundant, and handles many routes more efficiently.
FortiGate SD-WAN → Often uses OSPF internally and BGP externally to upstream providers, giving customers the best of both worlds.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 5
Q
A
Q: What is VLAN trunking (802.1Q)?
A:
VLAN (Virtual LAN): Logically separates traffic on the same physical network for security and efficiency.
802.1Q trunking: Standard for tagging VLAN traffic across trunk links, allowing multiple VLANs to share one physical uplink.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 6
Q
A
Q: What is STP/RSTP?
A:
STP (Spanning Tree Protocol): Prevents switching loops in a Layer 2 network by blocking redundant paths.
RSTP (Rapid STP): Faster convergence version of STP, reduces downtime during topology changes.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 7
Q
A
Q: Define IPSec, L2TP, GRE, and SSL/TLS in VPNs.
A:
IPSec: Encrypts IP traffic at Layer 3 (site-to-site, remote access).
L2TP (Layer 2 Tunneling Protocol): Provides tunneling; often paired with IPSec for security.
GRE (Generic Routing Encapsulation): Encapsulates packets, useful for multi-protocol tunnels, not secure by itself.
SSL/TLS VPN: Uses HTTPS (Layer 7), easy client access via browser, good for user-level remote access.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 8
Q
A
Q: Define NAT, DHCP, and DNS.
A:
NAT (Network Address Translation): Translates private IPs to public IPs for internet access.
DHCP (Dynamic Host Configuration Protocol): Automatically assigns IP addresses to devices.
DNS (Domain Name System): Resolves human-readable names (www.fortinet.com) into IP addresses.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 9
Q
A
Q: What is a wireless site survey?
A:
Assessment of an environment to design an optimal Wi-Fi deployment.
Identifies signal strength, interference, capacity requirements, and placement of APs.
Process of analyzing RF environment to determine optimal AP placement, channel selection, and power settings.
Tools: Ekahau, AirMagnet, Fortinet Survey tools.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 10
Q
A
Q: What is WPA2-Enterprise / 802.1X with RADIUS?
A:
WPA2-Enterprise: Secure Wi-Fi authentication using per-user credentials.
802.1X: Port-based network access control protocol.
RADIUS: Backend authentication server verifying user/device identity.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 11
Q
A
Q: Common Wi-Fi troubleshooting areas?
A:
Coverage gaps: Weak signal from poor AP placement.
Interference: Competing signals from other Wi-Fi or devices.
Authentication issues: Misconfigured RADIUS, certificates, or credentials.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 12
Q
A
Q: How does Fortinet integrate wireless into SD-WAN/NGFW?
A:
FortiAPs connect directly to FortiGate for secure WLAN.
Traffic is enforced with NGFW policies (IPS, filtering, VPN).
Centralized management via FortiManager.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 13
Q
A
Q: What is RADIUS?
A:
Authentication, Authorization, Accounting (AAA) protocol.
Validates users connecting to network services (VPN, Wi-Fi).
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 14
Q
A
Q: What is PKI?
A:
Public Key Infrastructure: Framework for managing digital certificates and encryption keys.
Enables authentication, encryption, and integrity for secure communications.
Uses digital certificates to verify identities and encrypt communication.
Components: CA (certificate authority), certificates, keys.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 15
Q
A
Q: What are MD5, SHA1, SHA2?
A:
MD5: 128-bit hash, broken.
SHA1: 160-bit hash, deprecated.
SHA2: Secure hashing family (SHA-256/512), current standard.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 16
Q
A
Q: What are DES, 3DES, and AES?
A:
DES: 56-bit symmetric cipher, obsolete.
3DES: Triple-encryption DES, stronger but inefficient.
AES: Modern symmetric standard (128/192/256-bit), fast and secure.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 17
Q
A
Q: What is the SSL/TLS handshake?
A:
Process where client and server agree on encryption method, exchange certificates, and establish secure session keys.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 18
Q
A
Q: What is IKE?
A:
Internet Key Exchange (IKE): A protocol that sets up security associations (SAs) for IPSec VPNs.
Negotiates encryption algorithms and keys.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 19
Q
A
Q: How do you qualify a lead technically?
A:
Discovery questions → identify business needs, pain points, current environment.
Align Fortinet solutions to measurable outcomes.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 20
Q
A
Q: How do you handle objections?
A:
Performance: Provide benchmarks, demos.
Cost: Focus on ROI and TCO savings.
Integration: Share reference architectures and customer success stories.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 21
Q
A
Q: What is your role post-sale as a Regional Systems Engineer?
A:
Be the customer’s technical advisor.
Deliver training and best practices.
Work with support/engineering on escalations.
Build trust → expansion and renewals.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 22
Q
A
Q: How do you adapt presentations to C-Level vs Engineers?
A:
C-Level: Business value, ROI, competitive differentiation.
Engineers: Technical deep dive, integration details, troubleshooting.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 23
Q
A
Q: How can stories help in technical sales?
A:
Real-world customer wins show credibility.
Example: AT&T $300M TCV growth using Fortinet/SD-WAN for healthcare.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 24
Q
A
Q: Why choose Fortinet over Palo Alto, Zscaler, Check Point?
A:
FortiOS + Security Fabric: Unified OS across portfolio enabling integrated management, automation, and threat sharing.
Broad portfolio (NGFW, SD-WAN, WLAN, SASE) all under one platform.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 25
Q
A
Q: What is FortiGate?
A:
Flagship NGFW with integrated SD-WAN, IPS, VPN, web filtering, and threat prevention.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 26
Q
A
Q: What is FortiAP?
A:
Wireless access points managed by FortiGate.
Provide secure Wi-Fi that inherits NGFW policies.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 27
Q
A
Q: What is FortiManager / FortiAnalyzer?
A:
FortiManager: Centralized management of Fortinet devices.
FortiAnalyzer: Log collection, analytics, reporting.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 28
Q
A
Q: What is FortiSASE?
A:
Fortinet’s Secure Access Service Edge offering.
Competes with Zscaler/Prisma by delivering cloud-based security and networking.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 29
Q
A
Q: Name three Fortinet products and their role.
A:
FortiGate: Next-gen firewall + SD-WAN.
FortiAP: Wireless access points.
FortiManager/FortiAnalyzer: Centralized management and analytics.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 30
Q
A
Q: What is Fortinet’s main differentiator?
A:
Single FortiOS operating system across the portfolio.
Integrated Security Fabric → better visibility, automation, TCO.
Interview Study Guide: Encryption and Advanced Technologies
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 31
Encryption
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 32
Interview Study Guide: Encryption and Advanced Technologies
Purpose:
Key Concepts:
Plaintext vs Ciphertext: Data before and after encryption.
Keys: Secret values used to lock/unlock data.
Symmetric Encryption: Same key for encrypt/decrypt (fast, e.g., AES).
Asymmetric Encryption: Public/private key pairs (RSA, ECC).
Hashing: One-way function for data integrity (SHA, MD5).
Digital Signatures: Prove authenticity + integrity with private/public key pairs.
Protect confidentiality, integrity, and authenticity of data.
1. Encryption Fundamentals
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 33
Interview Study Guide: Encryption and Advanced Technologies
Symmetric:
AES (Advanced Encryption Standard): Modern standard, 128/192/256-bit keys.
DES (Data Encryption Standard): Obsolete, weak.
3DES: Stronger than DES, but slow and outdated.
Asymmetric:
RSA: Common for key exchange, SSL/TLS certs.
Elliptic Curve Cryptography (ECC): Stronger security
Hashing Functions:
MD5: Broken, not secure.
SHA-1: Deprecated.
SHA-2 (SHA-256, SHA-512): Modern secure hashes.
2. Common Encryption Algorithms
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 34
Interview Study Guide: Encryption and Advanced Technologies
TLS/SSL (HTTPS):
Provides encryption for web traffic.
Uses asymmetric encryption (certificates) for handshake, symmetric for bulk data.
IPSec:
Encrypts traffic at network layer.
Protocols: ESP (encryption + integrity), AH (integrity only).
Uses IKE (Internet Key Exchange) to negotiate keys.
VPNs:
SSL VPN: Browser or client-based, often user-level remote access.
IPSec VPN: Site-to-site or full-tunnel remote access.
Wi-Fi Encryption:
WPA2-Enterprise (802.1X with RADIUS): Strong enterprise-grade Wi-Fi security.
WPA3: Newer, stronger standard with forward secrecy.
3. Encryption in Protocols
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 35
Interview Study Guide: Encryption and Advanced Technologies
PKI (Public Key Infrastructure):
Framework for issuing, distributing, and managing digital certificates.
Certificate Authorities (CAs): Trusted third parties issuing certs.
Certificates: Bind a public key to an identity.
Challenges in Sales Engineering:
Explaining why PKI matters (trust, scalability, compliance).
Positioning Fortinet’s certificate handling vs competitors.
4. Key Management & PKI
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 36
Threats to Encryption
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 37
Interview Study Guide: Encryption and Advanced Technologies
Brute force attacks:
Man-in-the-Middle (MITM):
Weak algorithms:
Key mismanagement:
Trying all possible keys.
Intercepting traffic if handshake isn’t validated.
DES, MD5, SHA-1 no longer secure.
Leaked keys, weak passwords, no rotation.
5. Threats to Encryption
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 38
Sales Engineer Angle
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 39
Interview Study Guide: Encryption and Advanced Technologies
Zero Trust + Encryption:
TLS inspection (SSL decryption):
Firewalls (like FortiGate) can decrypt SSL/TLS traffic, inspect for threats, then re-encrypt.
Sales Engineers
Forward Secrecy:
FIPS Compliance:
Encrypt everywhere, but still validate identity and device posture.
Must know how to explain privacy, compliance, and performance trade-offs.
Session keys are ephemeral; even if a key is stolen later, past traffic stays safe.
Required for government contracts.
6. Sales Engineer Angle
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 40
Interview Study Guide: Encryption and Advanced Technologies
How to Talk to Executives:
Focus on business risk: “Encryption ensures your customer data and IP stay confidential, keeping you compliant with HIPAA/PCI/GDPR.”
Mention compliance/regulations.
How to Talk to Engineers:
Discuss protocol support (IPSec, SSL/TLS, WPA2/WPA3), algorithm strengths (AES-256, ECC).
Show familiarity with TLS inspection, VPN designs, and certificate handling.
Stories You Can Use:
Add a story you can use around the tech that you are discussing.
Add a story you can use around the tech that you are discussing.
Sales Engineer Angle
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 41
Diffie-Hellman
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 42
Interview Study Guide: Encryption and Advanced Technologies
8. Diffie–Hellman
Diffie–Hellman (often written as DH) is a key exchange algorithm used in encryption. It’s not encryption by itself, but a method that allows two parties to agree on a shared secret key over an insecure channel (such as the internet), without actually sending the key itself.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 43
Interview Study Guide: Encryption and Advanced Technologies
How It Works (Simplified)
Both sides agree on two public numbers: a prime number (p) and a base (g).
Each side picks a private secret number (like a password).
They compute a public value using math (g^secret mod p) and exchange those public values.
Each side then raises the other’s public value to their private secret.
The math ensures they both end up with the same shared secret key, even though they never sent it directly.
Why It Matters
Prevents eavesdroppers from learning the shared key.
Forms the foundation for many secure protocols: TLS/SSL handshakes, IPSec, VPNs, WPA3 Wi-Fi.
Often used with Elliptic Curve Cryptography (ECDH) for stronger security with smaller keys.
Limitations
By itself, DH does not provide authentication.
Vulnerable to man-in-the-middle attacks if not combined with digital signatures or certificates.
That’s why you’ll see it used inside protocols (like TLS with certificates) rather than on its own.
For your interview:
If they ask about Diffie–Hellman, explain that it’s a secure way to generate a shared encryption key across an untrusted network, without transmitting the key. Then tie it back to VPNs (IPSec uses DH in IKE) or TLS handshakes—both highly relevant to firewall vendors like Fortinet.
8. Diffie–Hellman
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 44
Interview Study Guide: Encryption and Advanced Technologies
Classic (Finite Field) Diffie–Hellman
The original 1976 algorithm using modular arithmetic with large prime numbers.
Still used in some VPN/IPSec setups.
Requires large key sizes (2048+ bits) for modern security.
2. Ephemeral Diffie–Hellman (DHE)
Uses temporary (ephemeral) keys for each session.
Provides Perfect Forward Secrecy (PFS):
Common in TLS handshakes (TLS_DHE_RSA, TLS_DHE_DSS).
3. Elliptic-Curve Diffie–Hellman (ECDH)
Uses elliptic curve cryptography instead of modular arithmetic.
Much faster, smaller keys (256-bit ECC ≈ 3072-bit RSA security).
Widely used in TLS (ECDHE), mobile devices, VPNs.
4. Ephemeral Elliptic-Curve Diffie–Hellman (ECDHE)
Combines ECC + ephemeral keys.
Industry standard in modern HTTPS (TLS 1.2/1.3) and Fortinet NGFW/VPNs.
Provides both strong security and forward secrecy.
5. Authenticated Diffie–Hellman Variants
DH by itself doesn’t authenticate participants.
Variants include:
Station-to-Station (STS) Protocol: Adds authentication.
Authenticated DH in TLS/IPSec: Uses certificates or pre-shared keys for validation.
even if the long-term key is stolen later, past sessions remain secure.
8. Diffie–Hellman
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 45
Interview Study Guide: Encryption and Advanced Technologies
8. Diffie–Hellman
Summary
Main families:
Classic DH (finite field)
DHE (ephemeral)
ECDH (elliptic curve)
ECDHE (elliptic + ephemeral)
Practical takeaway for interviews:
Today, ECDHE is the gold standard (fast, secure, PFS).
Legacy systems may still use DHE or classic DH.
Always highlight Forward Secrecy as a key benefit when discussing DH in sales engineering.
What Diffie-Hellman really does!
It let’s two computers agree on a shared secret key over the internet.
That key is then used for encryption (like AES) to secure all further communication.
The trick: the key is never sent directly; only parts of the math puzzle are shared.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 46
Interview Study Guide: Encryption and Advanced Technologies
Diffie–Hellman Variants with Examples
1. Classic Diffie–Hellman (Finite Field DH)
Public values: prime number p = 23, base g = 5
Alice’s secret: a = 6
Bob’s secret: b = 15
Step 1: Alice computes A = g^a mod p = 5^6 mod 23 = 8 Bob computes B = g^b mod p = 5^15 mod 23 = 19
Step 2: Exchange public values: Alice sends 8, Bob sends 19.
Step 3: Alice computes s = B^a mod p = 19^6 mod 23 = 2 Bob computes s = A^b mod p = 8^15 mod 23 = 2
✅ Shared secret key = 2
2. Ephemeral Diffie–Hellman (DHE)
Same math as above, but keys are temporary (ephemeral).
Example: In HTTPS (TLS 1.2), every connection generates new random a and b → a unique secret key per session.
This gives Perfect Forward Secrecy (PFS): even if someone later steals the server’s private key, they can’t decrypt past sessions.
✅ Think of it as “classic DH, but throw away the keys after each conversation.”
3. Elliptic Curve Diffie–Hellman (ECDH)
Uses elliptic curve math instead of primes.
Example curve: secp256k1 (used in Bitcoin).
Alice picks a private key (say 3), Bob picks private key (say 7).
They multiply their private key by a common base point (G) on the curve.
Alice sends 3G, Bob sends 7G.
Alice computes 3(7G) = 21G, Bob computes 7(3G) = 21G.
✅ Shared secret = 21G (a point on the curve).
Advantage: Much smaller numbers for the same security (faster, efficient).
4. Ephemeral Elliptic Curve Diffie–Hellman (ECDHE)
Most common in TLS 1.2/1.3 today.
Same as ECDH, but new random private keys for every session.
Ensures forward secrecy + efficiency.
✅ Example: Your browser (Chrome) connecting to Fortinet’s website → negotiates a fresh ECDHE key so even if Fortinet’s server keys leak later, your past browsing stays safe.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 47
Interview Study Guide: Encryption and Advanced Technologies
Optional (Deep-Dive/Bonus Topics)
Post-Quantum Impact: DH/ECDH can be broken by quantum computers (Shor’s algorithm).
Industry is moving toward post-quantum cryptography (PQC).
Logjam Attack (2015):
Exploited weak DH parameters → why we now require 2048-bit or stronger primes.
Diffie–Hellman is how two sides securely agree on a shared key without transmitting it.
Modern networks use ECDHE for speed and forward secrecy
Fortinet Angle:
“FortiGate supports ECDHE in TLS inspection and IPSec VPNs.”
“Forward secrecy ensures customer data is safe even if long-term certs are compromised.”
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 48
TLS/SSL
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 49
Interview Study Guide: Encryption and Advanced Technologies
TLS 1.2 Handshake
Step 1 > ClientHello
Proposes TLS version, cipher suites, random number.
Step 2 > ServerHello
Chooses cipher suite, TLS version, sends random number + certificate.
Optionally sends ServerKeyExchange (for DH/ECDHE).
Step 3 > ClientKeyExchange
Client verifies certificate.
Sends key exchange material (RSA secret or ECDHE params).
Step 4 > Key Derivation
Both sides compute shared session key.
Step 5 > ChangeCipherSpec (Client)
Client signals switch to encrypted comms.
Step 6 > ChangeCipherSpec (Server)
Server signals switch to encrypted comms.
Step 7 > Secure Session Established
Data encrypted with symmetric algorithms (e.g., AES).
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 50
Interview Study Guide: Encryption and Advanced Technologies
TLS 1.3 Handshake
Step 1 > ClientHello
Proposes cipher suites + sends key share (ECDHE) immediately.
Step 2 > ServerHello
Picks cipher suite, returns its key share + certificate.
Step 3 > Shared Key Computation
Both sides instantly derive session key (forward secrecy by default).
Step 4 > Encrypted Extensions
Server sends additional parameters (encrypted).
Step 5 > Finished Messages
Both client and server send “Finished” messages encrypted with the new session key.
Step 6 > Secure Session Established
Communication begins with strong symmetric encryption (AES-GCM, ChaCha20).
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 51
AES-GCM
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 52
Interview Study Guide: Encryption and Advanced Technologies
AES-GCM Explained
AES
GCM
Advanced Encryption Standard, a block cipher that encrypts 128-bit blocks with 128/192/256-bit keys.
Galois/Counter Mode, an AEAD (Authenticated Encryption with Associated Data) mode of operation.
AES-GCM is everywhere in modern security (TLS, VPNs, disk encryption, cloud services). Let’s break it down in a way that clicks:
Put together, AES-GCM provides both confidentiality (encryption) and integrity (authentication) in one step.
1. Counter Mode (CTR) for Encryption
Instead of directly encrypting the plaintext, AES encrypts a counter value (a nonce + incrementing counter).
That produces a keystream which is XORed with the plaintext → ciphertext.
This makes it act like a stream cipher (fast, parallelizable).
2. Galois Field Multiplication for Authentication
While encrypting, GCM also computes an authentication tag.
It uses Galois field math (binary polynomial multiplication mod a fixed irreducible polynomial).
The tag ensures the ciphertext wasn’t tampered with.
3. Associated Data
GCM can also authenticate unencrypted headers (like IP addresses, sequence numbers).
Example: In IPsec, headers stay visible for routing but still get integrity protection.
4. Final Output
Ciphertext + Authentication Tag (e.g., 16 bytes).
Receiver uses the same key/nonce to decrypt and verify the tag. If the tag fails, the message is rejected.
Fast & Parallelizable
Combined Encryption + Authentication
Requirement
Common Tag Size
Works great on modern CPUs (AES-NI instructions).
One pass, less overhead.Nonce
Each key/nonce pair must be unique. Reuse can break security.
128 bits (but can be 96, 112, etc.).
Properties
How It Works (High Level)
What is AES-GCM?
In short: AES-GCM = AES in counter mode (fast encryption) + Galois field authentication (integrity). It’s efficient, secure, and the go-to choice for modern cryptography.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 53
PKI
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 54
What is PKI?
PKI is the framework that uses encryption, digital certificates, and trusted authorities to provide:
Authentication (Are you really who you say you are?)
Encryption (Can only the right party read the data?)
Integrity (Has the data been tampered with?)
Non-repudiation (Can’t deny you sent it).
It’s the backbone of secure internet traffic (HTTPS, VPNs, secure email, etc.).
Asymmetric Key Pairs
Public Key → Shared openly; used to encrypt or verify.
Private Key → Kept secret; used to decrypt or sign.
Certificate Authority (CA)
Trusted third party that issues and signs certificates binding a public key to an identity (e.g., a website or person).
Registration Authority (RA)
Validates identities before the CA issues a certificate.
Digital Certificates (X.509)
Contain identity info (e.g., domain name, organization), the public key, issuer info, validity period, and a digital signature from the CA.
Interview Study Guide: Encryption and Advanced Technologies
Core Components
How PKI Works (Step-by-Step)
Website Certificate
The public key is embedded in a certificate signed by a CA (like DigiCert).
Your browser connects and asks for the site’s certificate.
Browser checks:
Is the certificate signed by a trusted CA?
Certificate Validation
The web server has a public/private key pair.
Is it expired or revoked?
Key Exchange
Browser and server use the public key in the certificate to securely exchange a session key (used for faster symmetric encryption).
Secure Comms
Now both sides use that symmetric session key for encrypted data exchange (since symmetric encryption is faster).
Does the domain match?
Client Request
Web Security
Email Security
VPN Authentication
Code Signing
Smart Cards/ID badges
HTTPS/TLS certificates for websites.
S/MIME for signing /encrypting messages.
Certificates for user/ device authentication.
Verify software integrity and publisher.
PKI-backed auth for physical /logical access.
In short: PKI is the trust system that lets you verify identities and establish encrypted connections online, using a chain of certificates and trusted authorities.
Real World Uses
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 55
OSI Model
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 56
Interview Study Guide: Encryption and Advanced Technologies
OSI Model
What is the OSI Model?
The Open Systems Interconnection (OSI) Model is a conceptual framework developed by the International Organization for Standardization (ISO).
Its purpose is to standardize how different computer systems communicate over a network, ensuring interoperability between hardware and software vendors.
In plain English:
The OSI Model acts as a universal language for networking, allowing diverse devices, systems, and applications to “speak” to each other using agreed-upon rules known as protocols.
Purpose and Importance
Standardization: It provides a structured approach to designing and understanding network systems, so all vendors can create compatible networking products.
Troubleshooting: By dividing communication into seven layers, network engineers can isolate issues (e.g., “Is it a cabling issue at Layer 1 or a routing problem at Layer 3?”).
Interoperability: Ensures hardware and software from different manufacturers can work together.
Modularity: Each layer can evolve independently as long as it adheres to the same interface rules.
How It Works (Encapsulation & Decapsulation)
When sending data:
Each OSI layer adds its own header (and sometimes trailer) that contains control information.
This process is called encapsulation.
At the receiving end, the headers are removed (decapsulation) as data travels up the stack.
Example:
When you load a webpage:
Layer 7: Browser sends an HTTP request.
Layer 4: TCP segments it and ensures reliable delivery.
Layer 3: IP determines the route.
Layer 2: Ethernet encapsulates frames.
Layer 1: Bits travel across cable or Wi-Fi.
At the destination, each layer reverses the process.
Mnemonic to Remember the Layers
Top → Bottom: “All People Seem To Need Data Processing” (Application → Presentation → Session → Transport → Network → Data Link → Physical)
Bottom → Top: “Please Do Not Throw Sausage Pizza Away”
In Real-World Terms
Imagine sending a letter:
Application: You write the message.
Presentation: You translate it into a readable format (e.g., English).
Session: You agree when to talk and how long.
Transport: You break it into pages and ensure each arrives.
Network: The postal service decides the best route.
Data Link: The post office reads addresses and places stamps.
Physical: A delivery truck moves the envelope to the recipient.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 57
Interview Study Guide: Encryption and Advanced Technologies
OSI Model
Why the OSI Model Still Matters
Although modern networking — including the Internet — primarily follows the TCP/IP model rather than the original OSI structure, the OSI Model remains an essential conceptual tool for understanding and troubleshooting network communication.
The OSI Framework provides a layered and logical approach to identifying where problems occur within a network. By breaking communication into seven distinct layers, engineers and IT professionals can methodically isolate issues — whether they stem from physical connections, routing, encryption, or application-level services.
For example:
If a user can’t connect to Wi-Fi, the issue might be at Layer 1 (Physical) or Layer 2 (Data Link).
If a website is unreachable for thousands of users, the problem might be found at Layer 3 (Network) or Layer 7 (Application).
By pinpointing which layer is failing, teams can eliminate unnecessary troubleshooting steps, saving time and ensuring a structured path toward resolution.
In short, the OSI Model provides a universal language for diagnosing network issues, allowing diverse teams, tools, and technologies to communicate clearly and effectively.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 58
Interview Study Guide: Encryption and Advanced Technologies
OSI Model
OSI Layer | Functions | Common Protocols/Services | Encryption / Security Examples
Layer 7 – Application | User-facing apps, network services | HTTP/HTTPS, SMTP, IMAP, POP3, DNS, SNMP, FTP, SSH, Telnet | HTTPS (TLS), S/MIME (email), PGP (email), SSH, DNSSEC
Layer 6 – Presentation | Data formatting, compression, translation | JPEG, GIF, MPEG, XML, ASN.1 | TLS/SSL handshake, encryption/decryption, compression
Layer 5 – Session | Establish/manage/terminate sessions | NetBIOS, RPC, PPTP, SIP, SMB | TLS/SSL session keys, PPTP VPN (legacy), SIP over TLS
Layer 4 – Transport | End-to-end delivery, reliability | TCP, UDP | TLS/SSL (sits on TCP), QUIC (encrypted transport for HTTP/3)
Layer 3 – Network | Logical addressing, routing, path selection | IP, ICMP, RIP, OSPF, BGP | IPSec (ESP/AH), GRE (tunneling, no encryption by itself)
Layer 2 – Data Link | Frames, MAC addressing, error detection | Ethernet, ARP, PPP, 802.11 (Wi-Fi) | MACsec (802.1AE), WPA2/WPA3 (802.1X + RADIUS)
Layer 1 – Physical | Transmission of raw bits | Fiber optics, Ethernet cables, Wi-Fi radio signals | Physical security only (no encryption at this layer)
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 59
Advanced Networking
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 60
Interview Study Guide: Encryption and Advanced Technologies
Border Gateway Protocol
BGP stands for Border Gateway Protocol. It’s the standardized exterior gateway protocol used to exchange routing information between different autonomous systems (AS) on the Internet. In simple terms, BGP decides how data packets should travel across the web by choosing the best path between large networks.
Key Points:
Type of Protocol:
Purpose:
Decision Process:
Versions:
Reliability:
iBGP vs. eBGP:
eBGP
iBGP
Path-vector routing protocol.
Connects different autonomous systems (AS) — think of each AS as a separate “network under one administrative domain,” like an ISP or a large enterprise.
BGP doesn’t just look at the shortest path (like OSPF or RIP might). Instead, it uses attributes and policies (AS-Path, Local Preference, MED, etc.) to select the best route.
The main one used today is BGP-4, which supports Classless Inter-Domain Routing (CIDR) to help reduce the size of global routing tables.
BGP runs over TCP (port 179), ensuring reliable communication between routers.
Between different autonomous systems (external).
Within the same autonomous system (internal).
Why It Matters:
Without BGP, the Internet as we know it wouldn’t work — it’s the “postal service” that makes sure packets can leave one network (say, AT&T) and find their way to another (like Google).
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 61
Administrative Distance (AD)
iBGP: AD = 200 (less preferred than most IGPs like OSPF/EIGRP).
eBGP: AD = 20 (more preferred than iBGP).
Next-Hop Behavior
iBGP: By default, it does not change the next-hop attribute when advertising routes to internal peers. You often need to use next-hop-self.
eBGP: By default, it does change the next-hop to itself when advertising routes.
TTL / Hop Behavior
iBGP: Peers are expected to be reachable within the AS, so the TTL is usually 255 (must be directly reachable unless multihop is configured).
eBGP: Default TTL = 1, meaning peers are usually directly connected (but you can configure ebgp-multihop if not).
Route Propagation Rules
iBGP: Does NOT advertise routes learned from one iBGP peer to another iBGP peer (to avoid loops).
Requires full mesh (or route reflectors / confederations) for scalability.
eBGP: Advertises learned routes to other eBGP peers without restriction.
iBGP: Used to carry BGP routes across an AS, usually in combination with an IGP for next-hop reachability.
eBGP: Used to exchange routing information between different organizations/networks (e.g., between ISPs or ISP ↔ Enterprise).
Use Case
Interview Study Guide: Encryption and Advanced Technologies
Definition
iBGP (Internal BGP): Runs within the exact Autonomous System (AS).
eBGP (External BGP): Runs between different Autonomous Systems.
In short:
eBGP = External peering between ASes, lower AD, direct next-hop updates.
iBGP = Internal distribution within the same AS, higher AD, requires full mesh or route reflectors.
iBGP vs eBGP
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 62
Encapsulation
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 63
What is Encapsulation?
Encapsulation is the process of wrapping data with protocol information at each layer of the OSI or TCP/IP model as it moves down the stack (from the application the user sees, to the physical bits on the wire).
Think of it like putting a letter into envelopes:
The message is your data.
Each envelope adds addressing or handling instructions for the next stage.
At the destination, the receiver unpacks (decapsulates) the envelopes in reverse order.
1. Application Layer
Your data is generated (e.g., typing “Hello” into WhatsApp).
Protocol: HTTP, SMTP, DNS, etc.
Encapsulation: Adds application-specific headers.
2. Transport Layer
Decides how to deliver data (reliable TCP vs. fast UDP).
Encapsulation:
TCP header (port numbers, sequence numbers, reliability flags).
UDP header (port numbers, checksum, length).
Result = Segment (TCP) or Datagram (UDP).
3. Network Layer
Decides where the data goes (logical addressing).
Encapsulation:
IP header (source IP, destination IP, TTL, etc.).
Result = Packet.
4. Data Link Layer
Handles local delivery over a physical link.
Encapsulation:
Ethernet header (source/destination MAC address, type field).
Trailer (Frame Check Sequence for error detection).
Result = Frame.
5. Physical Layer
Converts the frame into bits (0s and 1s) and transmits them as electrical signals, light pulses, or radio waves over the medium.
Result = Bits on the wire.
Interview Study Guide: Encryption and Advanced Technologies
Step-by-Step Encapsulation (TCP/IP Stack Example)
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
Application
Presentation
Session
Transport
Network
Data Link
Physical
OSI Model Example of Encapsulation
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 64
SSE
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 65
SWG (Secure Web Gateway)
CASB (Cloud Access Security Broker)
ZTNA (Zero Trust Network Access)
DLP (Data Loss Prevention)
Threat Intelligence / Malware Inspection
Filters internet traffic, blocks malicious sites, and enforces acceptable use policies.
Protects use of SaaS apps (like Office 365, Salesforce, Google Workspace) by enforcing security policies, controlling data sharing, and preventing shadow IT.
Provides identity-based, least-privilege access to applications (instead of full VPN access). Verifies who you are, what device you’re on, and what you’re allowed to access.
(often included) Prevents sensitive data (PII, PHI, financial data, etc.) from leaving the network, whether in web uploads, SaaS apps, or email.
Uses sandboxing, AI/ML, and global threat feeds to stop advanced threats before they reach the endpoint.
Interview Study Guide: Encryption and Advanced Technologies
Core Components of SSE
Work-from-Anywhere
SSE delivers security directly from the cloud, no matter where the user connects.
Applications live in SaaS/IaaS (Office 365, AWS, etc.), so SSE protects access without forcing backhaul to HQ.
Zero Trust Alignment
Users don’t sit behind a corporate firewall anymore.
Instead of “connect first, then authenticate,” SSE enforces “authenticate and validate first, then connect.”
Cloud-first World
What is SSE?
Secure Service Edge (SSE) is a cloud-delivered security framework defined by Gartner in 2021. It provides security services for users, devices, and applications at the edge, close to where they connect to the internet, SaaS, or cloud resources—rather than backhauling all traffic through a traditional data center.
Think of it as the security half of SASE (Secure Access Service Edge).
SASE = Networking (SD-WAN) + Security (SSE)
SSE = Just the Security part
SSE (Secure Services Edge)
Why SSE Matters
Leading Vendors
In short: SSE is a cloud-native security service that replaces traditional on-premises appliances with a unified platform that delivers SWG, CASB, ZTNA, and DLP. It’s the security side of SASE, enabling secure, identity-driven access to apps and data from anywhere.
Chart: 
| Others | Fortinet | Palo Alto Networks | Netskope | Zscaler
Sales | 0.06 | 0.18 | 0.2 | 0.22 | 0.34
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 66
Interview Study Guide: Encryption and Advanced Technologies
Problem:
Users are everywhere (remote, hybrid, contractors), apps are in the cloud (SaaS/IaaS), and legacy VPN + firewalls can’t keep up.
Pain Points:
VPN sprawl, poor user experience. Shadow IT SaaS usage (unsanctioned apps). Compliance gaps (DLP, HIPAA, PCI).
Solution (SSE):
ZTNA: Replaces VPNs with least-privilege, identity-aware access.
CASB: Visibility + control of SaaS apps.
SWG: Inline protection against malicious sites.
DLP/Threat Intel: Protect sensitive data + stop malware.
Sales Engineer Angle (SSE)
SSE secures users and data everywhere — without slowing them down.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 67
Interview Study Guide: Encryption and Advanced Technologies
SSE (Secure Services Edge)
Conceptual Architecture
Internet
Public Cloud
Private Cloud
SaaS Services
Core Security Edge
Remote Users
Remote Site Type B
Remote Site Type A
Corporate Site & Datacenter
CASB
VPN GW East
VPN GW West
ISP Gateway
ISP Gateway
ISP Gateway
ZTNA
DLP
AV
Internet
SWG
IPSEC/GRE VPN
IPSEC/GRE VPN
IPSEC/GRE VPN
IPSEC/GRE VPN
Internal Routing
90 Locations Globally
15,000 In-office Users Globally
5000 Remote Users Globally
Operations: 24x7x365
32 Locations
3 Locations
55 Locations
API
API/Proxy
API/Proxy
API/Proxy
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 68
SASE
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 69
SD-WAN:
SSE (Security Service Edge):
Cloud-native delivery:
Zero Trust principles:
Identity + context-driven access instead of network trust.
Services delivered via distributed Points of Presence (PoPs).
SWG, CASB, ZTNA, DLP, threat protection (everything we just covered).
Dynamic, application-aware routing across WAN links (MPLS, broadband, LTE, 5G). Provides QoS, path selection, and WAN optimization.
Interview Study Guide: Encryption and Advanced Technologies
Core Components of SSE
Branch/remote
SD-WAN
SSE
Traffic
User traffic is steered to the nearest SASE PoP.
Component chooses best transport path (MPLS, DIA, LTE, etc.).
Component inspects/filters traffic (SWG, CASB, ZTNA, etc.).
Exits securely toward SaaS, cloud, or datacenter apps.
Definition
Coined by Gartner in 2019.
SASE = Networking + Security delivered as a cloud-native service.
Think of it as the fusion of SD-WAN (connectivity) + SSE (security).
SASE (Secure Access Services Edge)
How SASE Works
Leading Vendors
In short:
SSE = just the security stack.
SASE = SSE + SD-WAN networking.
If SSE is the “checkpoint in the cloud,” SASE is the checkpoint + highway system all in one service.
Chart: 
| Cato Networks | Versa Networks | Fortinet | Cisco | Palo Alto Networks | Zscaler
Sales | 0.07 | 0.09 | 0.12 | 0.2 | 0.22 | 0.3
Simplified architecture:
Fewer on-prem appliances (no separate WAN edge, VPN, firewall stacks).
Same security no matter if user is at branch, HQ, home, or roaming
Consistent policy:
.Reduced backhaul:
Internet/SaaS traffic goes direct-to-cloud via nearest PoP, not hairpinned through HQ.
Agility:
Spin up new branches/users faster.
Cost efficiency:
Replace MPLS with broadband + SASE.
Key Features
Multi-branch enterprises
Hybrid workforces
Any Organizations
Replacing MPLS with broadband + SASE.
Needing secure cloud access from anywhere.
Wanting unified network + security under a single service provider.
Use Cases
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 70
Interview Study Guide: Encryption and Advanced Technologies
Problem:
Pain Points:
Multiple vendor complexity (SD-WAN, firewalls, VPN, CASB, SWG).
Solution (SASE):
One Fabric: Combines SD-WAN (network) + SSE (security).
WAN + Security stacks
Inconsistent policies across regions.
Growing hybrid workforce.
Local Breakout: Traffic exits at nearest PoP → reduced latency.
Zero Trust: Identity-driven access everywhere.
Diverse technology stacks with multiple management console.
Multiple platform training and certification
Sales Engineer Angle (SASE)
SASE unifies networking and security in the cloud — one platform, one policy
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 71
Interview Study Guide: Encryption and Advanced Technologies
SASE (Secure Access Services Edge)
Conceptual Architecture
Internet
Public Cloud
Private Cloud
SaaS Services
ZTNA
DLP
AV
Core Security Edge
Remote Users
Remote Site Type B
Remote Site Type A
Corporate Site & Datacenter
CASB
SDWAN POP EAST
SDWAN POP WEST
Primary Fiber
Secondary LTE/5G
Secondary LTE/5G
Primary Fiber
Tertiary Broadband
Secondary LTE/5G
Primary Fiber
Network Fabric
R1
R2
R1
R2
R3
R1
R2
API
API/Proxy
API/Proxy
API/Proxy
32 Locations
3 Locations
55 Locations
90 Locations Globally
15,000 In-office Users Globally
5000 Remote Users Globally
Operations: 24x7x365
IPSec Tunnel
Internet
SWG
VPN
VPN
VPN
VPN
VPN
VPN
VPN
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 72
Legacy Networking
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 73
Interview Study Guide: Encryption and Advanced Technologies
1. Latency & Performance
Symptom: All branch/remote traffic is forced through HQ/datacenter before reaching the internet or SaaS.
Poor SaaS performance (O365, Salesforce, Zoom, etc.) when accessed via central breakout.
End-user frustration and degraded productivity.
2. Inefficient Bandwidth Usage
Symptom: Internet-bound traffic from branches uses expensive MPLS/private links to backhaul to HQ.
Drives up WAN costs.
Creates bottlenecks at datacenter internet egress points.
3. Scalability Challenges
Symptom: All security enforcement (firewalls, proxies, DLP) centralized at HQ.
Difficult to support cloud-first / SaaS-heavy environments.
Expansion to new branches requires complex MPLS provisioning.
4. Poor User Experience for Remote Work
Symptom: VPN users connect into HQ first, then hairpin out to SaaS or cloud.
Frustrates hybrid/remote workforce.
5. Limited Cloud/SaaS Optimization
Symptom: Legacy networks were designed for “inside-out” traffic (user → data center apps).
Cloud adoption breaks the hub-and-spoke model.
6. Single Point of Failure / Bottleneck
Symptom: Datacenter becomes the chokepoint for all traffic.
Creates a fragile architecture not fit for distributed enterprises.
Impact: Adds unnecessary hops → increases round-trip time.
Impact: Wastes bandwidth capacity.
Impact: Scaling requires adding more appliances and bigger links at the hub.
Impact: Sluggish performance, especially for video conferencing and collaboration tools.
Impact: Doesn’t optimize for “outside-in” (SaaS, cloud workloads, direct internet apps).
Impact: If HQ goes down, branch-to-cloud connectivity is disrupted.
Limitations of Backhauling Traffic in a Legacy Network
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 74
Interview Study Guide: Encryption and Advanced Technologies
1. Latency & Performance
Symptom: All branch/remote traffic is forced through HQ/datacenter before reaching the internet or SaaS.
Poor SaaS performance (O365, Salesforce, Zoom, etc.) when accessed via central breakout.
End-user frustration and degraded productivity.
2. Inefficient Bandwidth Usage
Symptom: Internet-bound traffic from branches uses expensive MPLS/private links to backhaul to HQ.
Drives up WAN costs.
Creates bottlenecks at datacenter internet egress points.
3. Scalability Challenges
Symptom: All security enforcement (firewalls, proxies, DLP) centralized at HQ.
Difficult to support cloud-first / SaaS-heavy environments.
Expansion to new branches requires complex MPLS provisioning.
4. Poor User Experience for Remote Work
Symptom: VPN users connect into HQ first, then hairpin out to SaaS or cloud.
Frustrates hybrid/remote workforce.
5. Limited Cloud/SaaS Optimization
Symptom: Legacy networks were designed for “inside-out” traffic (user → data center apps).
Cloud adoption breaks the hub-and-spoke model.
6. Single Point of Failure / Bottleneck
Symptom: Datacenter becomes the chokepoint for all traffic.
Creates a fragile architecture not fit for distributed enterprises.
Impact: Adds unnecessary hops → increases round-trip time.
Impact: Wastes bandwidth capacity.
Impact: Scaling requires adding more appliances and bigger links at the hub.
Impact: Sluggish performance, especially for video conferencing and collaboration tools.
Impact: Doesn’t optimize for “outside-in” (SaaS, cloud workloads, direct internet apps).
Impact: If HQ goes down, branch-to-cloud connectivity is disrupted.
Limitations of Backhauling Traffic in a Legacy Network
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 75
IPSec Tunnels
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 76
Interview Study Guide: Encryption and Advanced Technologies
IPSEC Tunnel Limitations
A. IKE_SA_INIT
B. IKE_AUTH
C. ESP Tunnel
D. CREATE_CHILD_SA
We agree how to talk securely.
We prove who we are and agree what traffic is protected.
We now actually protect the user data.
We keep it alive and fresh.
An IPsec (Internet Protocol Security) tunnel is a secure point-to-point link that provides confidentiality, integrity, and authentication for IP traffic across an underlying network. Establishing an IPsec tunnel involves negotiating encryption parameters, authenticating peers, and building security associations that define how traffic is protected and routed. The process can be summarized in the following steps:
Physical IP connectivity is established between the tunnel endpoints.
IKE (Internet Key Exchange) negotiates cryptographic algorithms, exchanges keys, and authenticates peers.
An IKE Security Association (SA) is created, followed by one or more IPsec SAs.
The IPsec SAs define encryption, integrity, and lifetimes for traffic flows (e.g., AES, SHA-2, Diffie-Hellman, PFS).
Traffic selectors are applied so only defined subnets/hosts use the tunnel.
Packets are encapsulated with ESP headers/trailers (or AH), encrypted, and transmitted securely across the network.
Rekeying, Dead Peer Detection, and delete messages manage tunnel lifecycle and resilience.
Each Step of the handshake initialization
IPSec VPN
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 77
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing an IPSec Tunnel
5. Lifecycle
Source Device
Destination Device
Transport
(Internet)
IPSec Tunnel
IPSec Tunnel
Internet
Internet
Public IP: 32.137.2.54
Public IP: 129.12.2.24
Network 10.1.1.0/24
Destination IP
10.1.1.1
Subnet
255.255.255.0
Network 10.10.10.0/24
Source IP
10.10.10.1
Subnet
255.255.255.0
1. Physical IP connectivity between tunnel endpoints.
  Ports/Protocols:
  UDP/500 → IKE (negotiation)
  UDP/4500 → NAT-T (when either side is behind NAT)
  ESP (IP protocol 50) → Data plane (unless encapsulated in UDP/4500 with NAT-T)
  Tunnel Interfaces created.
1. Physical IP connectivity between tunnel endpoints.
  Ports/Protocols:
  UDP/500 → IKE (negotiation)
  UDP/4500 → NAT-T (when either side is behind NAT)
  ESP (IP protocol 50) → Data plane (unless encapsulated in UDP/4500 with NAT-T)
  Tunnel Interfaces created.
2. IKEv2 Handshake (Control Plane)
2a. Phase 1: IKE_SA_INIT (2 messages)
2b. Phase 2: IKE_AUTH (2 messages)
3. Optional / Ongoing Control Messages.
4. Data Plane (ESP Tunnel)
4. Data Plane (ESP Tunnel).
6. Routing (static/dynamic) added to forward traffic into tunnel.
6. Routing (static/dynamic) added to forward traffic into tunnel.
An IPsec (Internet Protocol Security) tunnel is a secure point-to-point link that provides confidentiality, integrity, and authentication for IP traffic across an underlying network. Establishing an IPsec tunnel involves negotiating encryption parameters, authenticating peers, and building security associations that define how traffic is protected and routed.
The process can be summarized in the following steps:
2. IKEv2 Handshake (Control Plane)
2a. Phase 1: IKE_SA_INIT (2 messages)
2b. Phase 2: IKE_AUTH (2 messages)
3. Optional / Ongoing Control Messages.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 78
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing an IPSEC Tunnel 1. Pre-Work / Preconditions
IPs and Interfaces
Security policies
Shared credentials
Matching crypto proposals
(algorithms, lifetimes, DH groups).
(pre-shared key or digital certificates).
(which subnets, protocols, ports are protected).
Public IPs or reachable interfaces.
Both peers (e.g., branch firewall ↔ SASE PoP) must be configured with:
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 79
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing an IPSec Tunnel
2. Phase 1
Initiator sends a proposal
Responder replies with the accepted proposal.
Diffie-Hellman key exchange:
Both peers generate public/private DH keys and exchange public values.
They compute the shared secret independently.
Peer authentication:
Each side proves its identity (via pre-shared key, certificate, or EAP).
IKE SA established:
A secure, encrypted channel (ISAKMP SA) is now in place.
All further negotiation is protected inside this tunnel.
Encryption algorithm (AES, 3DES), hash (SHA), Diffie-Hellman group, and authentication method.
IKE (Internet Key Exchange) – Building the Secure Channel
This phase authenticates the peers and establishes a secure control channel.
Steps:
IKE SA negotiation begins:
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 80
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing an IPSec Tunnel
3. Phase 2
Negotiate IPSec parameters:
Encryption algorithm (AES-CBC, AES-GCM, ChaCha20, etc.).
Integrity/authentication (SHA-256, HMAC).
Perfect Forward Secrecy (PFS) if enabled (new DH exchange).
Establish IPSec SAs (Security Associations):
Two unidirectional SAs are created (one per traffic flow direction).
Each SA contains keys, algorithms, and lifetimes.
IPSec SA (Child SA) – Establishing Data Protection
This phase negotiates how actual traffic will be encrypted and encapsulated.
Steps:
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 81
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing an IPSec Tunnel 4. Encapsulation & Encryption of Traffic
Traffic match
ESP (Encapsulating Security Payload) or AH (Authentication Header):
ESP = encrypts payload + adds integrity/authentication.
AH = integrity/authentication only (rarely used today).
Encapsulation
Transmission
Original IP packet is encrypted and wrapped in a new IP header with ESP.
Encrypted packet is sent across the public internet to the remote peer.
Outbound packets are matched against crypto ACLs / security policies.
Once SAs are established:
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 82
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing an IPSec Tunnel 5. Decryption on the Receiving Side
Peer receives encrypted packet
Verify integrity/ authentication
Decrypt payload
Deliver original packet
Identifies correct SA via SPI (Security Parameter Index).
Using HMAC/SHA.
Using shared session keys.
To the internal network as if it were sent directly..
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 83
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing an IPSec Tunnel
End Result
Phase 1 (IKE SA)
Phase 2 (IPSec SA)
Data Flow
Creates a secure negotiation/control tunnel.
Defines how user data is encrypted and transmitted.
Cleartext inside local LAN ↔ encrypted ESP packets over internet ↔ cleartext again on remote LAN.
✅ End Result
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 84
Interview Study Guide: Encryption and Advanced Technologies
1. The Protocol Limit
Underlying link speed (e.g., 1 Gbps, 10 Gbps DIA/ISP link).
Device crypto performance (firewall/SD-WAN edge/PoP handling AES-GCM, SHA, etc.).
Tunnel overhead (~10–20% loss depending on ESP headers, NAT-T).
2. Real-World Device Limits
Branch/edge devices (Cisco ISR, Fortinet FortiGate, Palo Alto, Versa, etc.) often do ~500 Mbps – 2 Gbps IPSec per tunnel on mid-tier boxes.
Enterprise firewalls can push 10–20 Gbps per tunnel with hardware crypto acceleration (AES-NI, Cavium, etc.).
Carrier-grade appliances (Juniper, Cisco ASR, Fortinet high-end) can exceed 100 Gbps aggregate IPSec throughput, though usually spread across multiple tunnels/cores.
IPSec itself does not define a strict throughput cap.The tunnel’s maximum capacity is bounded by:
3. In a SASE/SD-WAN Context
Branch to PoP tunnels are typically IPSec VPNs.
Capacity is limited by branch device + ISP link, not the SASE cloud itself (PoPs are usually massively scalable).
Vendors encourage multiple tunnels (ECMP/load-balancing) to improve throughput and redundancy rather than maxing out a single IPSec session.
4. Rule of Thumb
Mid-tier branch CPE: ~1–5 Gbps max IPSec throughput.
Enterprise edge / DC firewall: ~10–40 Gbps per tunnel.
Carrier-grade / purpose-built crypto accelerators: 100 Gbps+ (aggregate).
5. Bottom line:
An IPSec tunnel doesn’t have a protocol-imposed max. In SASE/SD-WAN deployments, expect ~1–5 Gbps per branch tunnel, 10–40 Gbps.
On enterprise gear, and 100 Gbps+ on carrier-grade platforms — with scaling achieved by spreading traffic across multiple tunnels.
IPSEC Tunnel Limitations
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 85
GRE Tunnels
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 86
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing a GRE Tunnel
1. Define Tunnel Endpoints
Identify the source and destination IP addresses of the routers that will form the tunnel.
These are usually the public or reachable IP addresses on each router’s WAN interface.
2. Create a Tunnel Interface
On each router, configure a logical tunnel interface.
This is a virtual interface (e.g., Tunnel0) that represents the GRE tunnel.
3. Assign Source and Destination
Specify the tunnel source (local physical interface/IP) and the tunnel destination (remote router IP).
4. Select GRE as the Encapsulation
Define the tunnel mode as GRE.
By default, many vendors use GRE, but it can be explicitly configured.
5. Assign an IP Address to the Tunnel
Give the GRE tunnel interface an IP address on both ends.
These addresses form a logical point-to-point network that can run routing protocols.
6. Routing Over the Tunnel
Add static routes or enable dynamic routing protocols (OSPF, EIGRP, BGP, etc.) over the tunnel network.
Traffic destined for the remote network is forwarded into the tunnel interface, encapsulated with a GRE header, and sent to the remote endpoint.
7.Encapsulation/ Decapsulation Process
Encapsulation: Original packet → GRE header added → Outer IP header added → Sent across the underlying network.
Decapsulation: Remote router strips the outer IP and GRE headers → Forwards the original packet.
Important: GRE itself does not provide encryption. That’s why it’s often paired with IPSec → GRE over IPSec = encapsulation plus encryption for secure tunnels.
GRE is often used to encapsulate packets so they can traverse networks that don’t natively support those protocols, or to build logical point-to-point links.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 87
Interview Study Guide: Encryption and Advanced Technologies
Steps to Establishing a GRE Tunnel
7 GRE encapsulation/ decapsulation moves packets across the underlying network.
Source Device
Destination Device
Transport
(Internet)
GRE Tunnel
GRE Tunnel
Internet
Internet
Public IP: 32.137.2.54
Public IP: 129.12.2.24
Network 10.1.1.0/24
Destination IP
10.1.1.1
Subnet
255.255.255.0
Network 10.10.10.0/24
Source IP
10.10.10.1
Subnet
255.255.255.0
1. Physical IP connectivity between tunnel endpoints.
1. Physical IP connectivity between tunnel endpoints.
2. Tunnel interfaces created (Int 0/0)
2. Tunnel interfaces created (Int 0/0)
3. Tunnel source configured
5. Tunnel interfaces given IP addresses.
3. Tunnel destination configured.
5. Tunnel interfaces given IP addresses.
4. GRE encapsulation defined.
4. GRE encapsulation defined.
6. Routing (static/dynamic) added to forward traffic into tunnel.
6. Routing (static/dynamic) added to forward traffic into tunnel.
A GRE (Generic Routing Encapsulation) tunnel is a logical point-to-point link that allows packets to be encapsulated and carried across an underlying IP network. Establishing a GRE tunnel involves creating virtual interfaces, defining tunnel endpoints, and enabling routing so traffic can flow seamlessly between networks. The process can be summarized in the following steps:
PLEASE TAKE NOTE – GRE VPN TUNNELS ARE NOT INHERENTLY SECURE.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 88
Interview Study Guide: Encryption and Advanced Technologies
1. GRE in SD-WAN
2. Encryption Consideration
3. Vendor Examples
4. How it Fits into SASE
5. Answer in plain terms
GRE (Generic Routing Encapsulation) is lightweight and easy to deploy for tunneling traffic between SD-WAN edges and/or cloud security services.
Many vendors (e.g., Cisco, Fortinet, Versa, Zscaler integrations) allow GRE as a tunnel type because:
Some edge devices can process GRE faster (less crypto overhead).
It’s firewall/NAT friendly in many environments.
Plain GRE = no encryption — just encapsulation.
In a SASE/SSE context, where traffic security is mandatory, GRE is often paired with:
IPSec wrapping (GRE over IPSec) for confidentiality and integrity.
Or used only in scenarios where encryption is provided elsewhere (e.g., TLS/HTTPS apps).
It’s simpler than IPSec.
Zscaler Internet Access (ZIA): Supports GRE tunnels from branch firewalls/routers into their SSE cloud PoPs. Often used for performance (vs. IPSec).
Cisco Viptela/Versa/Prisma SD-WAN: Can support both IPSec and GRE tunnels. IPSec is preferred for encryption, GRE for performance.
Fortinet: Primarily IPSec, but can run GRE/IPSec if needed for specific integration.
Branch → SASE PoP:
Inside SASE fabric:
Tunnel can be GRE or IPSec. GRE often chosen for speed, IPSec for security.
Traffic is re-secured/inspected anyway (SWG, CASB, ZTNA, DLP), so GRE is acceptable if performance outweighs encryption needs.
Yes, SD-WAN sometimes uses GRE tunnels in SASE deployments, especially for branch-to-PoP traffic.
But since GRE doesn’t encrypt, it’s either combined with IPSec (GRE over IPSec) or limited to cases where encryption is handled elsewhere. Most vendors still recommend IPSec as default for SASE, with GRE as an optimization option.
GRE Tunnel Limitations
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 89
Network Segmentation
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 90
Interview Study Guide: Encryption and Advanced Technologies
Network Segmentation
What is Network Segmentation?
Network segmentation is the practice of dividing a computer network into smaller, isolated subnetworks (segments). Each segment acts as its own zone, separated by firewalls, VLANs, or access control policies. Instead of having a single flat network where every device can communicate with every other device, segmentation enforces boundaries to limit communication.
Think of it like dividing a building into locked rooms instead of one big open space—people only get access to the rooms they need.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 91
Interview Study Guide: Encryption and Advanced Technologies
How it works?
Logical segmentation:
Benefits (Pros)
Physical segmentation:
Microsegmentation:
Improved Security
Limits lateral movement for attackers—if one segment is breached, others remain safe.
Helps enforce “least privilege” by controlling which devices/users can access specific resources.
Supports compliance requirements (e.g., PCI DSS requires segmentation of payment card data systems).
Performance Optimization
Reduces broadcast traffic and network congestion.
Helps prioritize critical application traffic.
Simplified Monitoring & Troubleshooting
Makes it easier to detect unusual traffic patterns within smaller segments.
Provides better visibility into what’s happening in each zone.
Containment of Issues
Limits the spread of malware, ransomware, or misconfigurations.
Prevents a single failure from affecting the entire network.
A finer-grained approach (common in data centers and cloud environments) where policies are enforced down to the workload or application level.
Uses separate switches, routers, or firewalls for isolation.
Uses technologies like VLANs, subnets, and ACLs to separate traffic.
Drawbacks (Cons)
Increased Complexity
More planning, design, and ongoing management required.
Misconfigured rules can block legitimate traffic or create gaps.
Higher Costs
May require additional hardware (firewalls, routers) or advanced software licenses.
Time and labor costs for designing and maintaining segmentation policies.
Potential Performance Bottlenecks
If all traffic between segments must pass through a firewall or security appliance, it can create latency or throughput issues.
User/Operational Friction
Employees or apps may face access restrictions that feel inconvenient if not designed carefully.
Can require more exception handling.
Real-World Use Cases
Enterprise Security:
Data Centers/Cloud:
Industrial/OT Networks:
Regulatory Compliance:
Isolating HR, Finance, and Guest Wi-Fi networks.
Microsegmentation of applications and workloads to limit breach impact.
Separating production equipment from corporate IT traffic.
Keeping sensitive data (e.g., cardholder, medical, financial) in isolated environments.
Network Segmentation
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 92
Interview Study Guide: Encryption and Advanced Technologies
Network Segmentation Topology
VLAN 201
10.0.21.0/24
VLAN 200
10.0.20.0/24
VLAN 202
10.0.22.0/24
VLAN 203
10.0.23.0/24
VLAN 204
10.0.24.0/24
VLAN 205
10.0.25.0/24
VLAN 206
10.0.26.0/24
VLAN 207
10.0.27.0/24
WAN
WAN
WAN (VPN Concentrator)
VLAN 300
10.0.30.0/24
Remote User Europe
VLAN 303
10.0.33.0/24
Remote User
North America
VLAN 301
10.0.31.0/24
Remote User South America
VLAN 302
10.0.32.0/24
INTERNET
Cloud 1
VLAN 401
10.0.41.0/24
Cloud 2
VLAN 402
10.0.42.0/24
Cloud 3
VLAN 403
10.0.43.0/24
Leadership Team
Network Management
Servers and Network Devices
Human Resources
Finance
Operations
Physical Security and IOT
Voice over IP Network
Firewall
10.0.0.0/24
MOBILE IPSEC VPN
MOBILE IPSEC VPN
MOBILE IPSEC VPN
BRANCH OFFICE IPSEC VPN
BRANCH OFFICE IPSEC VPN
BRANCH OFFICE IPSEC VPN
BRANCH OFFICE IPSEC VPN
MOBILE IPSEC VPN
MOBILE IPSEC VPN
Internet Traffic
Internet Zone
Internal Zone
Assumptions
All traffic (internal & external) is encrypted in transit (AES-256 or stronger).
All internal data is encrypted at rest (AES-256 or stronger; HIPAA, PCI-DSS, NIST aligned).
Network fabric is powered by Layer 3 switching.
Diagram is logical; not all switches, routers, or trunking are shown.
Routing between VLANs occurs but is not depicted.
WAN/cloud icons represent VPN tunnels & VLAN routing, not physical devices.
External traffic terminates at VPN concentrator → inspected by edge firewall (DPI).
Inter-VLAN traffic is controlled by firewall/ACL policies.
Authentication is centralized (RADIUS, LDAP, AD).
Additional micro-segmentation may exist within technology stacks.
Legacy reference model for conceptual illustration only—not a modern best-practice design. Principles generalize, but Zero Trust/SSE/micro-segmentation implementations differ for stronger security and efficiency.
Legend
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 93
Interview Study Guide: Encryption and Advanced Technologies
Network Segmentation
Assumptions
All Traffic, internal and external, is 256-bit AES encrypted.
All network fabric is powered by Layer 3 switching.
Not all network devices are shown.
Each network includes a network switching fabric with VLAN routing and trunking.
Routing between segments is not shown in this drawing.
Icons labeled “WAN” in the external network represent VPN and VLAN routing to remote users, sites, and services. They do not represent any physical networking or security devices or services.
All traffic coming from the external network is encrypted and undergoes Deep Packet Inspection at the edge firewall, which receives traffic from the VPN Concentrator.
For the server and network device segmentation, there may be further micro-segmentation within the technology stacks not represented in this drawing.
All data within the internal zone is encrypted at rest using AES-256 or stronger, in alignment with industry best practices and compliance standards (HIPAA, PCI-DSS, NIST, etc.).
All authentication leverages centralized identity services (RADIUS, LDAP, or AD integration).
All external links terminate in encrypted tunnels (IPSec, SSL/TLS, or equivalent).
Inter-VLAN traffic is subject to firewall/ACL inspection at the routing layer.
“Never trust, always verify.”
No subnet, VLAN, or user segment is considered inherently trusted — not even inside the “internal zone.”
Every flow (north-south or east-west) must be authenticated, authorized, and inspected before being allowed.
Intra-VLAN Traffic (within the same VLAN)
Devices can still talk to each other at L2 unless you apply micro-segmentation (e.g., private VLANs, host isolation, hypervisor firewalls, NAC policies).
In Zero Trust, even within the same VLAN, security controls may apply (e.g., “Workstation A can’t talk to Workstation B directly without policy approval”).
Inter-VLAN Traffic (between VLANs)
By default, routed by an L3 switch or firewall.
In Zero Trust, you force that routing through a policy enforcement point (PEP), often a firewall with DPI or a micro-segmentation agent (like Illumio, Zscaler Workload Segmentation, NSX-T).
No “trusted subnet” assumption → every flow requires explicit policy.
Big Difference vs Traditional Network
Traditional:
“Internal VLANs are trusted.”
Inter-VLAN routing may bypass DPI for performance reasons.
Zero Trust:
No VLAN is inherently trusted.
Every flow is subject to policy + inspection (either at the network or host level).
In a Zero Trust design:
Intra-VLAN traffic can be restricted or inspected via micro-segmentation.
Inter-VLAN traffic must always pass through security measures (firewall, DPI, ZTNA policies, micro-segmentation tools).
The concept of a “trusted subnet” is eliminated — only explicitly allowed traffic flows.
Zero Trust Principle
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 94
Interview Study Guide: Encryption and Advanced Technologies
Network Segmentation Wireless Segmentation
802.1X + RADIUS (dynamic VLAN assignment)
SSID uses WPA2/WPA3-Enterprise.
Client authenticates (EAP-TLS/PEAP/etc.) to a RADIUS server (Cisco ISE, Aruba ClearPass, FreeRADIUS).
RADIUS returns attributes (e.g., Tunnel-Private-Group-ID) that tell the AP which VLAN to put the client in.
Decision can use user group, device type, posture, etc.
DHCP then comes from that VLAN’s scope; downloadable ACLs/roles can add per-user L3/L7 policy.
Best practice for “Zero Trust” Wi-Fi.
DPSK / PPSK / Identity PSK (per-device or per-user pre-shared keys)
One SSID; each user/device gets a unique PSK that maps to a VLAN and/or role.
Supported by Ruckus DPSK, Aruba PPSK, Meraki iPSK, Mist/Extreme equivalents.
Great for devices that can’t do 802.1X but still need segmentation without many SSIDs.
MAC Authentication Bypass (MAB) / MAC-based VLAN
AP sends the device MAC to RADIUS; if it matches, RADIUS returns a VLAN.
Works for “dumb” devices (badge readers, cameras), but MACs are spoofable—use only when you must, ideally with profiling and tight ACLs.
Multiple SSIDs, each statically tagged to a VLAN
Simple and universal, but every extra SSID wastes airtime. Try to keep ≤3–4 SSIDs total.
How the backhaul/trunks work
On the wired side, AP uplinks are typically a 802.1Q trunk (or an AP-to-controller tunnel) carrying all the VLANs you’ll assign.
In “bridge/local” mode the AP tags frames onto the switch trunk. In “tunnel/centralized” mode, client traffic is GRE/CAPWAP-tunneled to a controller/gateway where VLAN/ACLs are applied.
Ensure your switches/routers have DHCP helpers and routing for each client VLAN.
Roaming & design gotchas
Dynamic VLANs must exist wherever the client can roam (or use tunnel mode so the gateway is the L3 anchor).
Too many SSIDs = high beacon/management overhead, slower Wi-Fi.
MAC-based methods are weakest for security; prefer 802.1X or (next) PPSK/iPSK.
For true Zero Trust, pair VLANs with per-user/device policies (roles/ACLs) rather than relying on VLANs alone.
Quick setup blueprint (802.1X dynamic VLAN)
Create one “corporate” SSID (WPA2/WPA3-Enterprise).
Point it at your RADIUS (ISE/ClearPass/FreeRADIUS) with proper shared secret.
In RADIUS, build policies: if user in “Finance AD group” ⇒ return VLAN 30 + role “finance-acl”; if device = printer MAC OUIs ⇒ VLAN 50 + restricted ACL; etc.
Trunk the AP ports (or use controller tunnels) with allowed VLANs.
Configure DHCP scopes and IP helper-addresses for each VLAN on your L3 gateway/firewall.
Test with one user per group; verify they pull the correct IP and policies.
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 95
Secure Browser
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 96
Interview Study Guide: Encryption and Advanced Technologies
Secure Browser (concept)
A secure browser is a web client designed to minimize exposure to malicious content by isolating, controlling, or hardening how web code is executed. Instead of rendering untrusted code directly on the endpoint, it uses techniques such as sandboxing, virtualization, or remote browser isolation (RBI) to keep threats away from local systems.
Core mechanics:
Isolation: Web sessions run in a container, sandbox, or remote VM; only safe rendering data (pixels, streams) is delivered to the user device.
Policy enforcement: Controls like copy/paste restrictions, download blocking, and DLP integration.
Encryption: TLS ensures session confidentiality; integration with SASE/SSE for inline inspection.
Lifecycle: Each session can be ephemeral (destroyed after use) to eliminate persistence of malware.
Use case:
Prevent phishing and drive-by malware.
Enforce Zero Trust browsing (every session untrusted until verified).
Meet compliance by isolating risky categories (contractors, unmanaged devices, privileged users).
Secure Browser
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 97
Interview Study Guide: Encryption and Advanced Technologies
Secure Browser
Vendor / Solution | What they offer (browser isolation / secure browser component) | Notable features / differentiators
Menlo Security | Remote Browser Isolation / Secure Cloud Browser | Claims protection from phishing & evasive malware; full isolation of user browsing sessions. (Menlo Security)
Netskope | Remote Browser Isolation (RBI) as part of its SSE / SWG platform | Pixel-rendering of risky sites so malware never reaches the endpoint; unified policy engine. (Netskope)
Palo Alto Networks | RBI as part of their SASE / Prisma Access stack | Native integration with their security policies and near-native UX. (Palo Alto Networks)
iBoss | Browser Isolation (RBI) integrated into their platform | Streams only pixels; clientless experience; when a site is risky, users are auto-redirected to isolated session. (iboss.com)
Ericom Software | Remote Browser Isolation / Web Isolation | Renders content in virtual containers, streams safe output; integrates with their Secure Web Gateway offerings. (Ericom Software)
Versa Networks | Versa Remote Browser Isolation | Runs web content in a remote environment to shield endpoints and apply zero trust policies. (Versa Networks)
Keeper Security | Secure / Remote Browser Isolation (via Keeper Connection Manager) | Provides isolated web sessions, session recording/auditing, controlled web access. (Keeper® Password Manager & Digital Vault)
Other / Emerging / Legacy | Others mentioned in market guides | Authentic8 (Silo), Garrison, Cloudflare (as part of SSE), etc. (Solutions Review)
Here are several vendors/solutions that offer “secure browser” or remote browser isolation/browser isolation capabilities (i.e., isolating or sandboxing web sessions) — along with key differentiators you can call out in an interview:
What to highlight in your interview
These secure browser / isolation offerings are often packaged into larger SASE / SSE / SWG platforms (e.g., Palo Alto, Netskope) rather than standalone products.
The differentiators tend to revolve around latency / performance, user experience (how “native” the browsing feels), policy integration, scalability, and how aggressively they isolate (pixel streaming vs DOM sanitization).
Knowing a few names will allow you to ask: “Are we going to build or integrate with an existing secure browser / isolation vendor? Which one? What drove that choice (UX, cost, risk posture)?”
If you like, I can send you a comparative feature matrix (vendor vs vendor) so you can see which ones lead on performance, latency, policy, UX, and security. Do you want me to build that out?
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)

## Slide 98
Interview Study Guide: Encryption and Advanced Technologies
Secure Browser
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)
🎯 Top 20 Interview Q&As for Pre-Sales Engineers
(Quick-Reference Summary – Encryption & Advanced Technologies)
🔹 Networking & Routing
BGP vs OSPF: BGP = Internet-scale, policy-based; OSPF = enterprise-scale, cost-based, fast convergence.
VLAN Trunking (802.1Q): Tags VLAN traffic so multiple VLANs share one physical link.
STP/RSTP: Prevents loops; RSTP converges faster.
Encapsulation: Each OSI layer adds a header (like nested envelopes) to deliver data.
🔹 VPNs & Encryption
IPSec vs GRE: IPSec = encrypted, GRE = encapsulation only; combine for GRE-over-IPSec.
IKE: Negotiates encryption algorithms and keys for IPSec tunnels.
SSL/TLS Handshake: Client and server agree on ciphers, exchange certs, and derive session keys.
Diffie-Hellman / ECDHE: Secure key exchange — shared secret never transmitted.
AES-GCM: Modern standard providing both encryption and integrity in one pass.
PKI: Trust system using certificates, keys, and CAs to authenticate and encrypt securely.
🔹 Security Frameworks & Zero Trust
Network Segmentation: Divide network into zones to limit lateral movement.
SASE: SD-WAN + SSE (network + security in the cloud).
SSE: SWG, CASB, ZTNA, DLP — security delivered at the edge.
Zero Trust: “Never trust, always verify” — every user, device, and session authenticated.
Secure Browser: Isolates browsing sessions to protect from malicious content.
🔹 Wireless & Access Control
WPA2-Enterprise / 802.1X: Authenticates users via RADIUS — unique credentials per user.
Wireless Site Survey: Measures RF strength, interference, and placement for optimal coverage.
🔹 Sales Engineering Focus
Qualifying a Lead: Discovery → identify pain → map to solution value.
Handling Objections: Use ROI, benchmarks, and real customer wins.
Adapting Demos: C-Level = outcomes; Engineers = technical depth.
💡 Key Takeaway
“Interview success isn’t just knowing the tech — it’s showing how you turn it into business outcomes.”

## Slide 99
© 2025 Tony DeGonia. All Rights Reserved | Encryption & Advanced Technologies Interview Study Guide by Tony DeGonia (2025)